## Slide 1: Rethinking YANG-based Service and Network Management in the Era of Agentic AI
An investigation into how Agent-to-Agent (A2A) communications impact the traditional service, network, and device YANG model.

## Slide 2: Agenda
Background & Context
  Understanding the convergence of YANG data models and AI Agents in modern network management
Two workflow Examples
Core Challenges Analysis
  Deep dive into major gaps impeding the effective AI-YANG integration
Potential Solutions
  Exploring technical and architectural pathways to bridge the identified gaps
Open Discussion
  Interactive Q&A, feedback sharing, and collaborative idea exchange

## Slide 3: Background and Context
We are moving from model-driven automation to AGENTICOPS, where LLM-based agents interpret intent and execute complex workflows across heterogeneous layers.
What we are targeting is the full autonomy…this is the final objective.
We now have protocols defined, e.g., MCP, A2A, A2A is sending plain text…but we would still want to send YANG data
How we should Integrate YANG into A2A message?

## Slide 4: Objective
The goal is to open community discussion, not to finalize a solution
Not a redesign of YANG

## Slide 5: The RFC 8969 Paradigm for Model-driven Automation
Orchestrator
Controller
Network Devices
Device Modeling
Network Orchestration
Service Orchestration
Network Modeling
Service Modeling
Deterministic workflow
  Automation follows rigid, predefined workflows
  Hard-coded logic to map service->network->device layers
Highly Structured Interface & Data Modeling
  Mandates highly structured YANG data models for every layer
A Framework for Automating Service and Network Management with YANG

## Slide 6: From Static Pipeline to Agent Hierarchy
Orchestrator AI Agent(s)
parses NL intent → service orchestration
Agent-to Agent communication Protocol
Network AI Agent(s)
Network Orchestration
NETCONF / RESTCONF / Telemetry
Network Devices
execute changes, report results
If the pipeline is re-implemented with AI Agents at each/some layer…
What would change?
Interfaces between layers are no longer YANG-driven management protocols – it now travels alongside natural language intent, agent context, etc.
The workflow is done by a probabilistic reasoning engine, “some intent twice” may no longer mean “same device YANG configuration twice”
Operator Intent

## Slide 7
Workflow Example 1: intent-driven service provisioning / optimization
1
Operator intent
2
Orchestrator AI agent
3
Agent Communication
4
Network AI agent
5
Device execution
The network operator submits natural language service request
parses intents into a service model representation, confirms with the user, decomposes into structured network model based parameters
YANG-structured data + context metadata sent to network AI agent over Agent-to-Agent communication protocol
Converted to device model based configuration and delivered to network devices via protocols like NETCONF/RESTCONF
Devices apply the configuration change and report execution results back up the chain

## Slide 8
Workflow Example 2: Network Troubleshooting
1
Operational intent
Operator asks the agent to continuously monitor, diagnose, and autonomously repair issues.
2
Network operational state awareness
Agent grasps a holistic view of the network operational state
3
Diagnose & Plan
Once a fault is identified, the agent determines root cause and generates a targeted repair plan.
4
Simulate & Execute
Digital-twin simulation validates the fix, then the agent delivers YANG configuration changes to network devices.

## Slide 9: Core Challenges Analysis

## Slide 10: Gap Analysis 1: The Semantic Divide
Natural Language:
Pros
  Empowers human operators to express richer intent, e.g., expectations, constraints, preferences, retry strategies, and fallback rules
  Communication protocols like A2A natively support unstructured plain text
Cons:
  Could be ambiguous, and lacks the precision needed for network operations
Structured YANG:
Pros:
  ensure deterministic, high-efficiency execution with highly structured and validated schema
Cons:
  Completely inflexible and has expressiveness limits
The core challenge is translating high-level natural language negotiations into precise YANG representations without losing context.
Orchestrator Agents must prune and simplify intent to fit YANG data model

## Slide 11
Gap Analysis 2: Token Efficiency and Encoding Overhead
Key Concepts
LLMs don’t read text as humans do – they process tokens. Tokens are the basic units of text that LLMs process.
Each model has a maximum number of tokens it can handle (context window)
Both input (prompt + context) and output (responses) consumes tokens
LLM tokens cost money
Injecting verbose encoding into the LLM context window adds attention noise, latency, and cost without semantic payoff.
Structured formats (JSON/XML) often cost more tokens due to repeated field names/markup.
Highly compressed formats like CBOR solve bandwidth issues but are incompatible with LLMs (LLMs cannot consume raw binary payloads directly)

## Slide 12
Gap Analysis 3: Non-determinism Task Handling
Root-causes of Agent non-determinism
At the core, LLM runs on next-token prediction probabilities, which inherently introduces randomness.
Context drift: even minor shifts in historical context can alter outcomes for identical tasks.
Ambiguous natural language instructions
The same high-level intent can produce different YANG instance data across invocations; the same observed network state can yield multiple, distinct diagnostic trajectories and conclusions.
Key impacts of non-determinism on network operations
Undermined reliability
Reduced consistency
Increased operational complexity
Potential for harm
AI Agents introduces probability that challenge the deterministic foundations of model-driven networking.

## Slide 13: Potential Ways Forward

## Slide 14: Mapping Between the Four Paths and the Gaps
Possible Ways Forward
Gap 1
Semantic Divide
Gap 2
Token Efficiency
Gap 3
Non-determinism
① AI-Invocable Tools
✓
② Semantic Enhancement via Knowledge Graphs & Semantic Metadata
✓
③ Declarative Intent/Policy Overlay
✓
④ Token-Efficient YANG Serialization
✓

## Slide 15: YANG-driven Operations as AI-Invocable Tools
Agent
MCP Client
MCP Server
Tool examples:
get_devices_info
get_vpn_info
get_mpls_info get_interface_info
get_config_diff
commit_check
NETCONF/gNMI
Network
R1
R2
R4
R3
R5
MCP
Industry exploration:
https://github.com/jillesca/gNMIBuddy
https://github.com/Juniper/junos-mcp-server
Core idea:
refactor YANG-based network operations into AI-invocable tools using the Model Context Protocol (MCP)
The abstraction layer shields agents from low-level YANG syntax and schema complexity, reducing non-determinism risk

## Slide 16: Semantic Enrichment via Knowledge Graphs
Related IETF efforts:
https://datatracker.ietf.org/doc/draft-mackey-nmop-kg-for-netops/
https://datatracker.ietf.org/doc/draft-tailhardat-nmop-incident-management-noria/
https://datatracker.ietf.org/doc/draft-ietf-nmop-network-anomaly-semantics/
Core idea:
add a semantic layer on top of YANG data models to address YANG expressiveness limits via knowledge graph, which can explicitly model concepts absent from YANG, e.g., “preferred vs. optional” and “transient vs. persistent failure”
KGs give AI agents a machine-readable view of network semantics, relationships, and constraints. E.g., for the intent “check why the VPN tunnel is down,” a KG-enhanced agent queries relationships between the affected services and metrics
Network
R1
R2
R4
R3
R5
Operational State
Configuration
Knowledge Graph
KG builder
Semantic Agent Reasoning
Query

## Slide 17: Declarative Intent/Policy Overlay
YANG-structured payload + overlay
High-level Intent
Declarative Intent/Policy Overlay
Agent
Core idea:
  Instead of forcing agents to translate loose, high-level intent directly into rigid YANG leaf nodes, the agent first compiles the intent into a declarative intent/policy overlay
  The overlay could explicitly capture invariants, constraints, policies that existing YANG models cannot represent
  The overlay is co-delivered alongside the generated YANG instances to lower-layer agents
Industry exploration:
3GPP intent meta model
TMF intent management API
AI-driven Intent-Based Networking Approach for Self-configuration of Next Generation Networks
https://arxiv.org/html/2603.23772v1

## Slide 18: Token-efficient Data Format for LLM input? TOON?
TOON (Token-Oriented Object Notation)
  a data serialization format designed specifically for LLM applications.
  Zero syntax redundancy: removes closing XML tags and JSON braces
  Context window relief: 30%~60% less token consumption
  Official Repositories:
    https://github.com/toon-format/toon
    https://github.com/toon-format/spec
Format Comparison
{
"users": [
{
"id": 1,
"name": "Alice",
"role": "Admin",
"status": "Active"
},
{
"id": 2,
"name": "Bob",
"role": "User",
"status": "Inactive"
},
{
"id": 3,
"name": "Charlie",
"role": "User",
"status": "Active"
}
]
}
users[3]{id,name,role,status}:
1,Alice,Admin,Active
2,Bob,User,Inactive
3,Charlie,User,Active
JSON format
TOON format
TOON achieves 76.4% accuracy (vs JSON's 75.0%) while using 39.9% fewer tokens.
statistics source: https://github.com/toon-format/toon#benchmarks